| Status of ABB Issues on 01.07.15 |
| --- |
| Population: SR on 75 locomotives |
| SN | ITEM | STATUS |
| 1 | Hardware Issues |
| i | Failures of Power Module | PEBB Module failures high (25 in 14-15). Firm submitted analysis report indicating flaw in manufacturing process. Defective lot have been identified and replaced except in two locomotives in AQ & BIA sheds. |
| ii | Duagon Cards | Large no of Duagon card failures including modified Duagon card (D709). Firm mentioned failures due to Firmware malfunctioning. Firmware up-gradation has been done in 6 locos at AQ, TKD and GZB. Performance under observation. |
| iii | Failures of PEC800 cards | There had been 11 cases of PEC 800 cards during 14-15. Firm indicated that DOS file management system has been replaced with Reliance system and implemented in s/w version 35a11. So far updated in 68 locos. |
| iv | Breakage of cover support guide | Replacement of hardened steel dowel pins with Stainless Steel pins. To be completed by 31.05.15 as per MOM of TKD. Completed in 12 locomotives only. |
| v | Melting of float valve | Float valve gets stuck in orifice on top or bottom of level indicator and not visible thereafter. Float design ahs beep changed and replaced in 26 locomotives. |
| 2 | Software Issues |
| i | Implementation of DDS message in DIA card of VCU | DDS implementation trial is going on in 6 locos at different sheds for traction converter only. Implementation in aux converters is yet to be done. |
| ii | Time out initialization/time out release shut down | To be implemented in new software version. |
| iii | Regenerative braking issue during first instant | To be implemented in new software version. |
| iv | Time mismatch between converter & VCU | Time mismatch has been reduced to only 5-10 minutes. |
| v | LC Over current (both bogie getting isolated) | Demonstrated in AQ with Version 35 A11.Under observation. Completed in 68 locomotives. |
| vi | FLG-1 is not in service, change over to FLG-2 | To be implemented in new software version. |
| vii | Initialization time to be reduced to less than 50 seconds | Node 504 achieved in 60 seconds with modified PEC board on loco number 31471 at TKD and to be further reduced by 10 sec in second phase. |
| viii | Individual TM isolation on account of faulty speed sensor not possible | To be implemented in new software version. |
| ix | Converter redundancy demonstration for current measurement and DC link voltage measurement | Demonstrated in AQ with Version 35 A11.Under observation. Completed in 68 locomotives. |
| x | No Single point data down loading for traction converter and auxiliary converter | Implementation trial is going on 6 locos at different sheds for traction converter only. |
| xi | Unwanted Events | Demonstrated in AQ with Version 35 A11.Under observation. Completed in 68 locomotives. |
| xii | In case of Individual TM failure on line, there is no defined cause on driver display | Trial is going on 6 locos at different sheds along with DDS implementation. |
| xiii | Different software required with different make BUR | Pending |
| xiv | Sometimes message FLG1:0096 SS04 harmonic filter appear and filter cubicle isolate from service | To be implemented in new software version. |
| xv | Inspection and maintenance related issues | Stocking done at Nagpur, Delhi, Bangalore. Sheds to give feedback. |
| 3 | Miscellaneous |
| i | Loose Connection | FOC cable inspection process with "Intensity Instrument" meter implemented. Sheds to give feedback. |
| ii | While removing traction converter for any reason, TC to TC OFC is required to be removed by cutting connector. Firm to examine and suggests remedial measures | Pending |
| iii | Repair manual according to DDS | Not yet submitted. |