| Status of BHEL Issues on 01.07.15 |
| --- |
| Population: SR on 103 locomotives |
| SN | ITEM | STATUS |
| 1 | Hardware Issues |
| i | Failure of IGBT Power Module | 15 cases of power module failures occurred after P-3 modification. BHEL mentioned that 7 cases occurred due to poor workmanship. BHEL to submit detailed report to RDSO/CLW. No report submitted so far. |
| ii | Coolant leakage problem | Leakage in SR having cooling circuit with threaded joints. RDSO advised BHEL for using flanged coupling on trial basis in 10 locos. Performance to be monitored. |
| iii | High failure of DCU card in SR. | 25 failures occurred in 2014-15. BHEL to submit detailed report to RDSO/CLW. No report submitted so far. |
| iv | ACI card failure in AUX. converter. | Increase in failures of ACI cards in Aux. Converters. Firm has improved FPGA software to prevent boot loader error. BHEL to submit detailed report to RDSO/CLW. No report submitted so far. |
| 2 | Software Issues |
| i | ASC pulsing stop. | Problem increased after loading of software version 363. BHEL stated this occur in neutral section only. Modified s/w version 366 loaded in 31431/KYN and 5 locos in LGD shed. Performance under watch. |
| ii | Problem in harmonic filter isolation | Problem experienced after loading of software version 363 in 2 locos at LGD. BHEL to submit detailed report to RDSO/CLW. No report submitted so far. |
| iii | Healthiness of Battery charger | Message of Battery charger not working does not appear until battery voltage falls to 92 volts. BHEL to submit detailed report to RDSO/CLW. No report submitted so far. |
| 3 | Other Issues |  |
| i | Availability of Spare Parts & maintenance | Stocking has been done at three sheds having major population, lallaguda, kalyan and bhillai. Sheds to confirm the adequacy of spares. |
| ii | Commissioning failure | Commissioning failure still very high. 21 failures per 100 equipment commissioned at CLW during 2014-15. |
| iii | Training for trouble shooting, repair and maintenance. | Firm is required to submit the training calendar for zonal railways to CLW. |