| Status of ABB Issues on 01.09.15 |
| --- |
| Population: SR on 76 locomotives |
| SN | ITEM | STATUS |
| 1 | Hardware Issues |
| i | Failures of Power Module | PEBB Module failures high (25 in 14-15). Firm submitted analysis report indicating flaw in manufacturing process. Defective lot have been identified and replaced except 11 power modules in two locomotives in AQ & BIA sheds. Serial no. HKTX03 ans HKOD17 to be checked in 31470. |
| ii | Duagon Cards | Large no of Duagon card failures including modified Duagon card (D709). Firm mentioned failures due to Firmware malfunctioning. Firmware up-gradation has been done in 6 locos at AQ, TKD and GZB. Performance found satisfactory. So far, 52 locomotives have been modified. 12 Locos are pending for replacement by D709. |
| iii | Failures of PEC800 cards | There had been 11 cases of PEC 800 cards during 14-15. Firm indicated that DOS file management system has been replaced with Reliance system and implemented in s/w version 35a11. So far updated in 69 locos. Balance locos provided with s/w version 36. Railways to monitor the performance. |
| iv | Breakage of cover support guide | Replacement of hardened steel dowel pins with Stainless Steel pins. To be completed by 31.05.15 as per MOM of TKD. Completed in 30 locomotives only. Pins given to sheds for replacement. |
| v | Replacement of voltage sensor by LEM make | ABB make voltage sensors are to be replaced by LEM make. 3 locos are left for replacement. |
| 2 | Software Issues |
| i | Implementation of DDS message in DIA card of VCU | DDS implementation trial is going on in 6 locos at different sheds for traction converter only. Loco no 31611(TKD) has been provided with DDS implementation in SR and BUR. ABB to provide modified s/w version 36 in 3 locos at TKD (31545,30396, 30397) and 4 locos at BIA (30385, 30387, 31401, 31539) to monitor the performance for regular release of s/w ver.36. |
| ii | Time out initialization/time out release shut down | To be implemented in new software version. Issue to be resolved.ABB has captured data, analysis to be done. |
| iii | Regenerative braking issue during first instant | To be implemented in new software version. Implemented in Loco 31545 (TKD) and 30385 (BIA). |
| iv | Time mismatch between converter & VCU | Resolved in version 36.Under trial in TKD and BIA. Railways to monitor performance and give feedback to RDSO/CLW. |
| v | LC Over-current (both bogie getting isolated) | Resolved in version 36.Under trial in TKD and BIA. Railways to monitor performance and give feedback to RDSO/CLW. |
| vi | FLG-1 is not in service, change over to FLG-2 | To be studied in detail. |
| vii | Initialization time to be reduced to less than 50 seconds | Node 504 achieved in 60 seconds with modified PEC board on loco number 31471 at TKD and to be further reduced by 10 sec in second phase. |
| viii | Individual TM isolation on account of faulty speed sensor not possible | Resolved in s/w version 36. 7 locos have been modified in TKD and BIA. No problem experienced so far. |
| ix | Converter redundancy demonstration for current measurement and DC link voltage measurement | Demonstrated in AQ with Version 35 A11.Under observation. Completed in 68 locomotives. |
| x | No Single point data down loading for traction converter and auxiliary converter | ABB to upload modified s/w version 36 in 07 locos and monitor the performance. |
| xi | Unwanted Events | Resolved in version 36 except Invalid ID. Under trial in TKD and BIA. |
| xii | In case of Individual TM failure on line, there is no defined cause on driver display | Resolved in version 36.Under trial in TKD and BIA. |
| xiii | Different software required with different make BUR | Pending |
| xiv | Sometimes message FLG1:0096 SS04 harmonic filter appear and filter cubicle isolate from service | Resolved in version 36.Under trial in TKD and BIA. |
| xv | Inspection and maintenance related issues | Stocking done at Nagpur, Delhi, Bangalore. Sheds to give feedback. |
| 3 | Miscellaneous |
| i | While removing traction converter for any reason, TC to TC OFC is required to be removed by cutting connector. Firm to examine and suggests remedial measures | Pending |
| ii | Repair manual according to DDS | Not yet submitted. |
| i | While removing traction converter for any reason, TC to TC OFC is required to be removed by cutting connector. Firm to examine and suggests remedial measures | Pending |